Extraction recovery vanadylporphyrin complexes from the oil “North Buzachi”

Smaiyl Madi Bekezhanuly, Seisembekova Anar Bauyrzhankyzy

Master student 2nd year, PhD

Al-Farabi Kazakh National University,

Faculty chemistry and chemical technology, Almaty, Kazakhstan

E-mail: seysembekovaanar@gmail.com

High-viscosity heavy oils concentrate sulfur and metals with a high content of vanadium and nickel in metalloporphyrin forms, and one of the most common forms of petroleum metalloporphyrins is vanadylporphyrins. These compounds are catalytic poisons for oil refining processes and thus contribute to high-temperature corrosion of equipment surfaces, reducing the service life of turbojet, diesel and boiler plants [1-3].

In the present work, the extraction recovery of porphyrin complexes from the oil of the North Buzachi deposits (Kazakhstan) was carried out with the aim of their further use for the synthesis of catalytic systems.

To extract free porphyrin complexes, the oil sample, freed from water and mechanical impurities, was sequentially extracted with ten portions of solvent (DMFA, ethanol, acetone, acetonitrile) taken in the amount of 25 % by volume of oil. The obtained extracts were washed with water, followed by drying with sodium sulfate, the solvent was distilled under vacuum, then to identify the composition and determine the types of porphyrins in the obtained extracts, their adsorption chromatographic fractionation was carried out on a column with ASCG grade silica gel, followed by spectrophotometry.

Thus, the process of extraction porphyrin complexes of vanadium from oil and gas regions “North Buzachi”. It was found that when extracting porphyrin complexes, the yield of vanadylporphyrin complexes using as extractants was: ethanol 42.1 %; acetone 33.3 %; acetonitrile 56.1 % and DMFA 75.7 %. It is proved that the chromatographic separation of vanadylporphyrin complexes of North Buzachi oils reveals seven main fractions representing all types of known oil porphyrin structures with a predominance of ethio–, rodo – and DPEP types with four absorption maxima at 500 nm, 530 nm, 570 nm and 590 nm.

ACKNOWLEDGMENTS

The work was supported by the Ministry of Science and Education of the Republic of Kazakhstan (project AP08856825-OT-20 dated 01.10. 2020, "The use of vanadium porphyrins extracted from Kazakhstani oils for the catalytic processing of petroleum products").

References

- H.S. Silva, A.C.R. Sodero, J.P. Korb, A. Alfarra, P. Giusti, G. Vallverdu, D. Begue, I. Baraille, B. Bouyssiere, The role of metalloporphyrins on the physical-chemical properties of petroleum fluids, Fuel 188 (2017) 374–381.

- Wandekoken, F. G., Duyck, C. B., Fonseca, T. C. O., & Saint’Pierre, T. D. Method for the quantification of vanadyl porphyrins in fractions of crude oils by High Performance Liquid Chromatography–Flow Injection–Inductively Coupled Plasma Mass Spectrometry. Spectrochimica Acta Part B: Atomic Spectroscopy / Spectrochimica Acta Part B 119 (2016) 1–9

- Luz, M. S., & Oliveira, P. V. (2019). Non-chromatographic method for separation and determination of Fe, Ni and V porphyrins in crude oil / Talanta 199 (2019) 147–154